## Slide 1: DEPI project
A detailed breakdown of network architecture, configuration, and testing
Date
1- يوسف ممدوح رمضان عبد النبي applying the project in packet tracer 2-عمار زاهر أبو اليذيد handling the topology and the architecture of the project 3-علي فاروق علي محمدي handling the IPs configurations and subnetting 4-ادهم ايمن محمد test the project and the devices from topology to connectivity
5- عصام عبدالنبي سيد

## Slide 2: Introduction to the Project
• Overview of the campus network layout (ISP router, main buildings, branch office)
• Use of OSPF routing protocol and Router-on-a-Stick architecture for inter-VLAN communication
• Purpose: Distribute network traffic efficiently across multiple VLANs and ensure connectivity between all departments and buildings of our company
• Departments and VLAN distribution across the campus (HR, Admin, Finance, Business, IT, Students, etc.)

## Slide 3: Man1 (Ammar): Topology and Architecture
• ISP Router: Responsible for routing between the campus network and external cloud services
• Router-on-a-Stick: Configuration to handle inter-VLAN routing for the three main buildings and the branch office
• Layer 3 Switches: Used to manage intra-building VLAN traffic and provide routing capabilities
• Building and Department Distribution:
- Building A: HR, Admin, Finance, and Business departments
- Building B: E&C and A&D departments
- Building C: IT and Student Lab departments
- Branch: Staff and Students departments
• Justification: The architecture is designed for efficient traffic management, allowing for segmentation of traffic based on departments and providing flexibility for future expansion

## Slide 4: Man 2(ALI) : IP Addressing and Configuration
• VLAN IP Assignment:
- Building A: 192.168.1.0/24 (HR), 192.168.2.0/24 (Admin), etc.
- Building B: 192.168.5.0/24 (E&C), 192.168.6.0/24 (A&D)
- Building C: 192.168.7.0/24 (Student Lab), 192.168.8.0/24 (IT)
- Branch Office: 192.168.9.0/24 (Staff), 192.168.10.0/24 (Students)
• Router and Switch IPs: Subinterface IPs on the ISP router, Layer 3 switch, and branch router
• OSPF Configuration: Steps to configure OSPF for inter-VLAN and inter-building routing, ensuring proper communication across all VLANs
• Server IP Configuration: FTP server (192.168.8.10), Web server (192.168.8.11)

## Slide 5: Man 3 (Youssef): Network Setup in Cisco Packet Tracer
• Router-on-a-Stick Configuration: Show how VLANs are created on the ISP router with subinterfaces
• Layer 3 Switch Configuration: VLAN assignments, port configurations, and enabling routing
• Branch Router Configuration: Subinterface configuration for VLANs 90 and 100
• Server Setup: Configuration of FTP and Web servers in Building C (IT department)
• Visual Aid: A screenshot of the network setup from your Packet Tracer file (insert the diagram image from your project)

## Slide 6: Man 4(Adham) : Connectivity Testing and Verification
• Ping Tests: Testing connectivity between PCs within the same VLAN and across different VLANs
• OSPF Routing Verification: Checking OSPF neighbors and routes to ensure correct routing
• Server Testing: FTP and Web server access from different VLANs
• Remote Branch Connectivity: Testing connectivity between main campus and the branch office
• Redundancy and Failover Testing: Simulating link failures and verifying OSPF rerouting
• Broadcast Containment: Ensuring broadcast traffic stays within the correct VLANs

## Slide 7: Conclusion and Results
• Successful Network Implementation: All departments can communicate efficiently, both within and across VLANs
• Testing Results: All devices connected, servers accessible, and remote branch fully integrated
• Future Recommendations: Possible future upgrades and optimizations for scalability
• Thank You: A thank you message to the team for their hard work