## Slide 1
Project Title:
Network Infrastructure Project: HQ and Branch Office.
Subtitle:
Designing and Implementing a Scalable Network.
Presented by
[Mekawy Team].
Date:
[19/10/2024].

## Slide 2
Project Overview
Objective:
  To establish network infrastructure connecting the HQ and branch office.
Scope:
  HQ with segmented networks using VLANs.
  Branch office connectivity and local DHCP services.
Goals:
  Ensure communication between HQ and branch.
  Maintain network segmentation and performance.

## Slide 3
HQ Network Architecture
Overview:
  The HQ consists of a main router managing 8 networks, each corresponding to a VLAN.
  Each VLAN has its own dedicated switch for isolation and security.
VLAN Details:
  VLAN IDs: 10, 20, 30, 40, 50, 60, 70, 80,90,100.
  Each VLAN serves a specific purpose (e.g., IT, HR, finance, business, student lap, ).
Configuration:
  DHCP service is configured on the main router, providing IP addresses for each VLAN.

## Slide 4
HQ Router and VLAN Configuration
Router Configuration:
  Inter-VLAN routing enabled for internal communication .
  DHCP pools defined for each VLAN subnet.
  Ospf routing protocol defined for connecting the HQ to the branch
Switch Configuration:
  Access ports configured between the multilayer switch and VLAN-specific switches.
  Access ports assigned to specific VLANs for end devices.

## Slide 5
Branch Office Network Architecture
Overview:
  The branch office has a router that connects to the HQ router via ospf.
  The branch router has a DHCP service managing two local networks.
Connectivity:
  Routed link established between HQ and branch for secure communication.
Configuration:
  The branch router provides IP addresses and default gateways for the two local networks.

## Slide 6
Branch Router and Network Configuration
WAN Configuration:
  WAN interface connects to the HQ with site-to-site VPN encryption.
  Dynamic routing (e.g., OSPF) ensures traffic flow between HQ and branch.
  DHCP Configuration:
  Two networks configured with separate DHCP pools for IP address management.

## Slide 7
Network Connectivity and Communication
Inter-Site Routing:
  Routing tables on both HQ and branch routers configured to support communication between VLANs and branch networks.
Testing and Validation:
  Devices in all networks receive DHCP leases.
  Ping tests confirm connectivity within VLANs and between HQ and branch networks.